## Slide 1: IoT with ESP8266
Week of Learning 2018
Rick Suel
Paul Goodjohn

## Slide 2: Class Materials
The source code and presentation for this course can be found here: https://github.com/rdsuel/esp-class

## Slide 3: The ESP8266
http://esp8266.github.io/Arduino/versions/2.0.0/doc/reference.html
http://esp8266.net/

## Slide 4: Class Pre-Work
Install latest Arduino software from:
  https://www.arduino.cc/en/Main/Software
Install the Silicon Labs virtual com port (VCP) driver for your laptop’s operating system. This driver will allow your computer to recognize the ESP8266 device as a “com port” when you plug it in via USB.
  https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
Create an account on Adafruit IO. This is the cloud platform we will be using:
  https://io.adafruit.com/
Create an account on IFTTT. We will be using this platform to create events based on your device:
  https://ifttt.com/

## Slide 5: Setup (Continued)
Install the ESP8266 boards package:
  Tools  Board  Boards Manager

## Slide 6: Setup (Continued)
Configure the connection parameters for the device:
  Board: “Generic ESP8266 Module”
  Flash Size: 4M (1M SPIFFS)
  Flash Mode: “DOUT”
  Reset Method: “nodemcu”
  Port: choose the one for your device

## Slide 7: Install Arduino Libraries
We will need several libraries installed for this class:
Display Library (“ssd1306”):
Temp Sensor Libraries (“DHT” and “adafruit unified sensor”):

## Slide 8: Install Arduino Libraries (Continued)
NTP Client Library for getting time over the internet:
Adafruit MQTT Library for sending data to https://io.adafruit.com

## Slide 9: Exercise 1: Blinky
Goal:
Confirm you are able to load applications to your device by blinking the on-board LED.
Steps:
Load the ESP8266  Blink example.
Switch over to the “scheduler-based” blink architecture. This will serve as the platform for the future exercises.

## Slide 10: Exercise 2: Connect to Wifi
Goal:
Connect your device to the ”iot_class” network and print your IP address to the serial window.
Steps:
Update the “student.ino” template file so that it connects to the “iot_class”network. The password is “password”, so obviously it is very secure!
Once the device is connected, print the IP address to the serial window.
Congratulations, your esp8266 is now online. We’ll do more with this connection shortly!

## Slide 11: Exercise 3: OLED Display
Goal:
Add support for the OLED display and display the current by pulling it from the internet using an NTP server (time.nist.gov). Update the time every second.
Steps:
Wire the ESP8266 to the display as defined here:
Periodically read the time from the NTP server and write it to the display.
ESP8266 | Display
GPIO5 | SDA
GPIO4 | SCK
3.3V | VDD
GND | GND

## Slide 12: Exercise 4: DHT22 Temp/Humidity Sensor
Goal:
Add support for the DHT22 Temp/Humidity sensor. Display the temperature and humidity along with the current time on the OLED display.
Steps:
Wire the ESP8266 to the sensor as defined here:
Periodically read the temperature and humidity, and write them to the display.
ESP8266 | Sensor
GPIO0 | DAT
3.3V | VCC
GND | GND

## Slide 13: Exercise 5: Adafruit IO Cloud Platform
Goal:
Use MQTT to publish temperature and humidity values to the Adafruit IO platform, and create a GUI for displaying them.
Steps:
Log into https://io.adafruit.com.
Create a feed called “temperature”.
Create a feed called “humidity”.
Create a dashboard called “IoT Class”.
Add blocks to the dashboard for temp/humidity.
Add MQTT/adafruit support to your sketch.
Compile and upload to your device.

## Slide 14: Exercise 6: IFTTT Humidity Alerts
Goal:
Create an IFTTT “applet” to send you a text message (or email) when the humidity exceeds 70%.
Steps:
Log into your https://ifttt.com account
Create this new applet: