## Slide 1: IoT with ESP8266
Week of Learning 2018

## Slide 2: Class Materials
The source code and presentation for this course can be found here: https://github.com/rdsuel/esp-class

## Slide 3: The ESP8266
TBD – Add some background on the device

## Slide 4: Class Pre-Work
Install latest Arduino software from:
  https://www.arduino.cc/en/Main/Software
Install the Silicon Labs virtual com port (VCP) driver for your laptop’s operating system. This driver will allow your computer to recognize the ESP8266 device as a “com port” when you plug it in via USB.
  https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
Create an account on Adafruit IO. This is the cloud platform we will be using:
  https://io.adafruit.com/
Create an account on IFTTT. We will be using this platform to create events based on your device:
  https://ifttt.com/

## Slide 5: Setup (Continued)
Install the ESP8266 boards package:
  Tools  Board  Boards Manager

## Slide 6: Setup (Continued)
Configure the connection parameters for the device:
  Board: “Generic ESP8266 Module”
  Flash Size: 4M (1M SPIFFS)
  Flash Mode: “DOUT”
  Reset Method: “nodemcu”
  Port: choose the one for your device

## Slide 7: Install Arduino Libraries
We will need several libraries installed for this class:
Display Library (“ssd1306”):
Temp Sensor Libraries (“DHT” and “adafruit unified sensor”):

## Slide 8: Install Arduino Libraries (Continued)
NTP Client Library for getting time over the internet:

## Slide 9: Exercise 1: Blinky
Goal:
Load the built in “blink” application for the ESP8266 to your device and confirm that blue LED blinks.
This exercise confirms that everything is configured properly and ensures you can download and run an application.

## Slide 10: Exercise 2: Connect to Wifi
Goal:
Connect your device to the ”iot_class” network and print your IP address to the serial window.
Steps:
Update the “student.ino” template file so that it connects to the “iot_class”network. The password is “password”, so obviously it is very secure!
Once the device is connected, print the IP address to the serial window.
Congratulations, your esp8266 is now online. We’ll do more with this connection shortly!

## Slide 11: Exercise 3: OLED Display
Goal:
Add support for the OLED display and display the current time using the NTPClient library (grab current time from the internet).
Steps:
Wire the ESP8266 to the display as defined here:
Set up the NTPClient to pull the current time from
Write the time to the display periodically.
SDA
SCK
GND
VDD
ESP8266 | Display
GPIO3 | SDA
GPIO1 | SCK
3.3V | VDD
GND | GND

## Slide 12: Exercise 4: DHT22 Temp/Humidity Sensor
Goal:
Add support for the DHT22 Temp/Humidity sensor. Display the temperature and humidity along with the current time on the OLED display.
Steps:
Wire the ESP8266 to the sensor as defined here:
Periodically read the temperature and humidity from the sensor.
Write the temperature and humidity to the display periodically
ESP8266 | Sensor
GPIO4 | DAT
3.3V | VCC
GND | GND

## Slide 13: Exercise 5: Adafruit IO Cloud Platform
Goal:
Use MQTT to publish temperature and humidity values to the Adafruit IO platform, and create a GUI for displaying them.
Steps:
Add step one here.
And step two here.
And step three here, etc.

## Slide 14: Exercise 6: Adafruit IO Cloud Platform
Goal:
Use MQTT to publish temperature and humidity values to the Adafruit IO platform, and create a GUI for displaying them.
Steps:
Add step one here.
And step two here.
And step three here, etc.

## Slide 15: Exercise 2: Connect to Wifi
Goals: Get con
Step 1: Run the “WifiScan” example ensuring wifi works.
Step 2: Update the connect to the
Run the serial monitor, making sure that it is set to 115200 baud
You should see results like this:

## Slide 16: Exercise 2: OLED Display
Goal:
Get the OLED display connected and display your name on it.
Libraries:
SSD_1306

## Slide 17
So first we need the wifi library
Now we have to connect using those:
Now we need the wifi network SSID and password:
Finally let’s print out the IP address we were given:

## Slide 18: Exercise 4: DHT22 Sensor
To connect to the sensor you need the DHT library as well as the unified sensor library:

## Slide 19
Connect the GND to GND, VCC to 3.3v and DAT to GPIO4 with the wires
Add the libraries to the code and set it up
Add code to start the sensor up
Add variables to stick the data in
And get the data from the sensor
So you should be able to print out the temperature and humidity now

## Slide 20: Exercise 5: Cloud Platform

## Slide 21: Exercise 6: IFTTT